## Slide 1: COGO
C. Intersections
N, E
N, E
N, E

## Slide 2
1. Solution Logic
  Point whose position is to be computed has two unknowns: N and E.
  To solve those unknowns requires two measurements from one or more known positions.
    dist and dir from A to C
C
A
(N,E)

## Slide 3
1. Solution Logic
  Point whose position is to be computed has two unknowns: N and E.
  To solve those unknowns requires two measurements from one or more known positions.
    dist and dir from A to C or dist & dir from B to C
C
A
(N,E)
B
(N,E)

## Slide 4
1. Solution Logic
  Point whose position is to be computed has two unknowns: N and E.
  To solve those unknowns requires two measurements from one or more known positions.
or some combination – as long as it’s two measurements
(simultaneous solutions can get messy...)
C
A
(N,E)
B
(N,E)

## Slide 5
1. Solution Logic
  COGO Intersection uses a triangle:
  Two known points
    Base line – one side of the triangle
  A measurement from both ends to a third unknown point
    Two additional triangle parts
  Solve remaining triangle parts
    Forward comp to unknown point.
A
(N,E)
B
(N,E)
C
Base line

## Slide 6
2. Intersection Types
  The three primary intersection methods are:
- Distance-Distance
- Direction-Distance (angle-distance)
- Direction-Direction (angle-angle)
  In the following explanations, points A and B have known coordinates and serve as a base line.
A
(N,E)
B
(N,E)
C
Base line

## Slide 7
2. Intersection Types
a. Distance-Distance Intersection
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C
dAC
dBC
Known: (NA,EA) (NB,EB)

## Slide 8
2. Intersection Types
a. Distance-Distance Intersection
Two possible locations for point C.
Only one is the right one.
Pick it.
Note these triangles are mirrored.
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dAC
C2
dAC
dBC
dBC
Known: (NA,EA) (NB,EB)

## Slide 9
2. Intersection Types
a. Distance-Distance Intersection
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dBC
dAC
Known: (NA,EA) (NB,EB)

## Slide 10
2. Intersection Types
Inverse B to A
a. Distance-Distance Intersection
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dAC
dBC
DirBA, dBA
Known: (NA,EA) (NB,EB)

## Slide 11
2. Intersection Types
Inverse B to A
Law of cosines to solve for Angle B
a. Distance-Distance Intersection
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dAC
dBC
DirBA, dBA
Known: (NA,EA) (NB,EB)

## Slide 12
2. Intersection Types
a. Distance-Distance Intersection
Inverse B to A
Law of cosines to solve for Angle B
Use DirBA and Angle B to get DirBC
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dAC
dBC
DirBC,
DirBA, dBA
DirBC
Known: (NA,EA) (NB,EB)

## Slide 13
2. Intersection Types
a. Distance-Distance Intersection
Inverse B to A
Law of cosines to solve for Angle B
Use DirBA and Angle B to get DirBC
Forward comp from B to get C
Distance from A to C: dAC
Distance from B to C: dBC
A
B
C1
dAC
dBC
DirBC,
DirBA, dBA
DirBC
Known: (NA,EA) (NB,EB)

## Slide 14
2. Intersection Types
a. Distance-Distance Intersection
Distance from A to C: dAC
Distance from B to C: dBC
Inverse B to A
Law of cosines to solve for Angle B
Use DirBA and Angle B to get DirBC
Forward comp from B to get C
Math Check(s)?
A
B
C1
dAC
dBC
DirBC,
DirBA, dBA
Known: (NA,EA) (NB,EB)

## Slide 15
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
A
B
C
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 16
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Two possible locations for point C.
A
C1
dAC
C2
dAC
B
DirBC
Known: (NA,EA) (NB,EB)

## Slide 17
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
A
C1
C2
dAC
B
DirBA, dBA
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 18
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
A
C1
C2
dAC
B
DirBA, dBA
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 19
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Select correct angle
A
C1
C2
dAC
B
DirBA, dBA
?
?
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 20
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Select correct angle
A
C1
B
DirBA, dBA
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 21
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Compute Angle A from
  Angles B & C
A
C1
B
DirBA, dBA
dAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 22
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Compute Angle A from
  Angles B & C
Law of sines to solve dBC
A
C1
B
DirBA, dBA
dAC
dBC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 23
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Compute Angle A from
  Angles B & C
Law of sines to solve dBC
Forward comp from B to get C
A
C1
B
DirBA, dBA
dAC
dBC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 24
2. Intersection Types
b. Direction-Distance Intersection
Distance from A to C: dAC
Direction at B to C.
Inverse B to A
Compute Angle B from
  DirBA and DirBC
Law of sines to solve Angle C Compute Angle A from
  Angles B & C
Law of sines to solve dBC
Forward comp from B to get C
Math Check(s)?
A
C1
B
DirBA, dBA
dAC
dBC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 25
Only a single intersection.
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 26
Inverse from A to B
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
DirAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 27
Inverse from A to B
Compute Ang A from DirAC & DirAB
Compute Ang B from DirAC & DirBA
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
DirBC
DirAC
Known: (NA,EA) (NB,EB)

## Slide 28
Inverse from A to B
Compute Ang A from DirAC & DirAB
Compute Ang B from DirAC & DirBA
Compute Angle C from Angles A & B
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
DirAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 29
Inverse from A to B
Compute Ang A from DirAC & DirAB
Compute Ang B from DirAC & DirBA
Compute Angle C from Angles A & B
Law of sines to compute dAC
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
dAC
DirAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 30
Inverse from A to B
Compute Ang A from DirAC & DirAB
Compute Ang B from DirAC & DirBA
Compute Angle C from Angles A & B
Law of sines to compute dAC
Forward comp from A to get C
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
DirAC, dAC
DirAC
DirBC
Known: (NA,EA) (NB,EB)

## Slide 31
2. Intersection Types
c. Direction-Direction Intersection
Direction at A to C.
Direction at B to C.
A
C
B
DirAB, dAB
DirAC, dAC
DirAC
DirBC
Inverse from A to B
Compute Ang A from DirAC & DirAB
Compute Ang B from DirAC & DirBA
Compute Angle C from Angles A & B
Law of sines to compute dAC
Forward comp from A to get C
Math Check(s)?
Known: (NA,EA) (NB,EB)

## Slide 32
(1) Arc-Arc (Circle-Circle) intersection
  Same as Distance-Distance intersection.
  A and B are radius points.
2. Intersection Types
d. Other Intersections
A
B
C
C
R
b
R
b
R
a
R
a

## Slide 33
2. Intersection Types
(2) Arc-Direction (Circle-Direction) intersection
  Same as Distance-Direction intersection.
  A is radius point.
d. Other Intersections
A
C1
RA
C2
RA
B
DirBC

## Slide 34
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
Angle at S instead of a direction.
Angle-Distance intersection is variation of Direction-Distance intersection.
Solution logic is the same.

## Slide 35
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
a. Inverse TS
426.383
Az 246°18’44”

## Slide 36
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
426.383
Az 246°18’44”
75°24’23”
a. Inverse TS
b. Compute angle G
  Law of Sines
    Check if G < 90°

## Slide 37
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
a. Inverse TS
b. Compute angle G
  Law of Sines
c. Compute angle T
  Angle condition

## Slide 38
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
a. Inverse TS
b. Compute angle G
  Law of Sines
c. Compute angle T
  Angle condition
d. Compute AzTG
  Use AzTS & angle T
292°34’21”

## Slide 39
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”
a. Inverse TS
b. Compute angle G
  Law of Sines
c. Compute angle T
  Angle condition
d. Compute AzTG
e. Compute coords of G from T
  Forward Comp
833.92’ N
265.31’ E

## Slide 40
3. Example 1
What are the coordinates of G?
  Forward comp from T
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21” Az
833.92’ N
265.31’ E
a. Inverse TS
b. Compute angle G
  Law of Sines
c. Compute angle T
  Angle condition
d. Compute AzTG
e. Compute coords of G from T
  Forward Comp
f. Math check – Compute:
  SG by Law of Sines
  AzSG using AzTS & angle S
  Coords of G from S

## Slide 41
4. Example 2
What are the coordinates of 101?
  Forward comp from 30
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101

## Slide 42
4. Example 2
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
721.709’
298°57’39.0”
What are the coordinates of 101?
  Forward comp from 30

## Slide 43
4. Example 2
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
Step (2)
Compute angle at 30 by Law of Cosines
721.709’
298°57’39.0”
30°51’10.6”
What are the coordinates of 101?
  Forward comp from 30

## Slide 44
4. Example 2
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
Step (2)
Compute angle at 30 by Law of Cosines
Step (3)
Compute direction from 30 to 101
  Use Az30-20 & angle at 30
721.709’
298°57’39.0”
30°51’10.6”
559.83’
268°06’28.4”
What are the coordinates of 101?
  Forward comp from 30

## Slide 45
4. Example 2
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
Step (2)
Compute angle at 30 by Law of Cosines
Step (3)
Compute direction from 30 to 101
Step (4)
Forward comp from 30 to 101
721.709’
298°57’39.0”
30°51’10.6”
559.83’
268°06’28.4”
4574.616'N
1085.955'E
What are the coordinates of 101?
  Forward comp from 30

## Slide 46
4. Example 2
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
Step (2)
Compute angle at 30 by Law of Cosines
Step (3)
Compute direction from 30 to 101
Step (4)
Forward comp from 30 to 101
Math Check:
Compute coords from 20.
721.709’
298°57’39.0”
30°51’10.6”
559.83’
268°06’28.4”
4574.616'N
1085.955'E
What are the coordinates of 101?
  Forward comp from 30

## Slide 47
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
What are the coordinates of P?
  Forward comp from H
5. Example 3

## Slide 48
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (1) Inverse H to L
542.292’
Az 259°47’14”
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 49
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (2) Compute angle H
542.292’
Az 259°47’14”
41°07’16”
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 50
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (2) Compute angle H
Step (3) Compute angle L
542.292’
Az 259°47’14”
41°07’16”
51°02’04”
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 51
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (2) Compute angle H
Step (3) Compute angle L
Step (4) Compute side angle P
542.292’
Az 259°47’14”
41°07’16”
51°02’04”
87°50’40”
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 52
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (5) Compute side HP
542.292’
Az 259°47’14”
41°07’16”
51°02’04”
87°50’40”
421.944’
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 53
L
1715.50' N
646.00' E
H
1811.65' N
1179.70' E
300°54'30"
28°45'10"
P
Step (6) Compute P from H
542.292’
Az 259°47’14”
41°07’16”
51°02’04”
87°50’40”
421.944’
5. Example 3
What are the coordinates of P?
  Forward comp from H

## Slide 54
Ta-Daa!!

## Slide 55
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G

## Slide 56
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
a. Inverse TS

## Slide 57
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
a. Inverse TS
426.383
Az 246°18’44”

## Slide 58
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
b. Compute angle G
426.383
Az 246°18’44”

## Slide 59
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
b. Compute angle G
426.383
Az 246°18’44”
Makes sense.
Remember it could
be either G or 180°-G
75°24’23”

## Slide 60
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
c. Compute angle T
426.383
Az 246°18’44”
75°24’23”

## Slide 61
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
c. Compute angle T
426.383
Az 246°18’44”
75°24’23”
46°15’37”

## Slide 62
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
d. Compute Az TG
426.383
Az 246°18’44”
75°24’23”
46°15’37”

## Slide 63
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
d. Compute Az TG
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”
Add angle T because we turn to the right from TS to TG

## Slide 64
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
e. Compute coordinates of G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”

## Slide 65
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
e. Compute coordinates of G
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”

## Slide 66
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
f. Math check?
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”
833.92’ N
265.31’ E

## Slide 67
3. Example 1 - Complete Solution
What are the coordinates of G?
S
518.68' N
221.12' E
T
689.98' N
611.58' E
58°20'00"
375.00'
G
f. Math check?
426.383
Az 246°18’44”
75°24’23”
46°15’37”
292°34’21”
833.92’ N
265.31’ E
Compute:
  SG by Law of Sines
  Az SG using Az TS & angle S
  Coords of G from S

## Slide 68
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101

## Slide 69
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (1)
Inverse along the base line 30 to 20
721.709’
298°57’39.0”

## Slide 70
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (2)
Compute angle at 30 by Law of Cosines
721.709’
298°57’39.0”

## Slide 71
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (2)
Compute angle at 30 by Law of Cosines
721.709’
298°57’39.0”

## Slide 72
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (3)
Compute direction from 30 to 101
721.709’
298°57’39.0”
30°51’10.6”

## Slide 73
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Step (3)
Compute direction from 30 to 101
Angle at 30 is negative because we turn to the left from 30-20 to 30-101
Step (4)
Forward comp from 30 to 101
721.709’
298°57’39.0”
30°51’10.6”

## Slide 74
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
721.709’
298°57’39.0”
30°51’10.6”
4574.616'N
1085.955'E
Step (3)
Compute direction from 30 to 101
Angle at 30 is negative because we turn to the left from 30-20 to 30-101
Step (4)
Forward comp from 30 to 101

## Slide 75
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Math Check? Compute coords from 20.
721.709’
298°57’39.0”
30°51’10.6”
4574.616'N
1085.955'E

## Slide 76
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Math Check? Compute coords from 20.
Step (1) Compute angle at 20 by Law of Sines.
721.709’
298°57’39.0”
30°51’10.6”
4574.616'N
1085.955'E

## Slide 77
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Math Check? Compute coords from 20.
Step (1) Compute angle at 20 by Law of Sines.
721.709’
298°57’39.0”
30°51’10.6”
4574.616'N
1085.955'E

## Slide 78
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Math Check? Compute coords from 20.
Step (2) Compute direction from 20 to 101.
721.709’
298°57’39.0”
30°51’10.6”
49°58’37.4”
4574.616'N
1085.955'E

## Slide 79
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
Math Check? Compute coords from 20.
Step (2) Compute direction from 20 to 101.
Angle 20 is positive since we turn to the right from 20-30 to 20-101.
Step (3)
Forward comps from 20.
721.709’
298°57’39.0”
30°51’10.6”
49°58’37.4”
4574.616'N
1085.955'E

## Slide 80
4. Example 2 - Complete Solution
What are the coordinates of 101?
559.83'
374.91'
20
4942.56'N
1014.02'E
30
4593.10'N
1645.48'E
101
721.709’
298°57’39.0”
30°51’10.6”
49°58’37.4”
4574.616'N
1085.955'E
Math Check? Compute coords from 20.
Step (2) Compute direction from 20 to 101.
Angle 20 is positive since we turn to the right from 20-30 to 20-101.
Step (3)
Forward comps from 20.
check