## Slide 1: Mentoring Mondays, 13 Sep 2021 Conflicting Title Elements: Rules of Construction
Jerry Mahun, PLS
jerrymahun.com
Home | Mentoring Mondays | Rules of Construction
password: monday_roc
Typos in original Powerpoint. Corrected version uploaded Mon 13 Sep 10:00 am CDT

## Slide 2
The original Spice Girls?

## Slide 3: Learning Objectives
How parcels and boundaries are created
Where the Rules of Construction come from
What are unwritten rights
How gaps and overlaps are handled
The Statute of Frauds and why it matters
Description interpretation issues: Ambiguities; Controlling/informative terms
Written intent conflicts

## Slide 4: Just enough to be dangerous...
A ~40 slide Powerpoint doesn’t make you a description interpretation expert.
This material is a general overview with a lot of caveats because it is based on common law.
Common law can vary between jurisdictions; must be familiar with your area.
Often there is no definitive solution to a re-establishment problem, only the “best” given the circumstances.
Changing evidence even a little can dramatically affect the conclusion.
Research is key, including a title search back to parcel beginnings and parol evidence.
Consider all reasonable alternatives and why they do or don’t apply.

## Slide 5: I. Parcel Creation
A. What, Why?
  Parent-Child
    At least one new boundary
    Possible shared boundaries
    Multiple children, multiple new boundaries – how do they relate?
  Family analogy
    Child inherits characteristics from parent
    Parent must provide for child
Parent
Child
A
Parent
Child
A
Child
D
Child
B
Child
C

## Slide 6: I. Parcel Creation
B. Processes
  How boundaries are created affect:
    Description type
    How are gaps and overlaps handled
  Boundary creation
    Establishes boundary once and forever.
    Creates adjoiner relationship
    Location is “without error.”
    Creates evidence framework for later re-establishment.
  Creation methods
    Simultaneous
    Sequential
    Combination

## Slide 7: I. Parcel Creation
B. Processes
  1. Simultaneous
    Boundaries created at the same time by the same legal instrument. Have equal standing - no Sr-Jr relationships.
Lot 1
Lot 2
Lot 3
Lot 6
Lot 5
Lot 4
Section
Description types
Lot and block
Aliquot part

## Slide 8: I. Parcel Creation
B. Processes
  2. Sequential
    New parcels created independently from same parent over time.
    Earlier created boundaries have precedence (senior) over later created ones (junior).
Parent
Parcel
Parcel 3
2015
Parcel 1
2008
Parcel 2
2010
Jr
Sr
Jr Jr
Sr Sr
Description types
Metes
Bounds
Metes and Bounds

## Slide 9: I. Parcel Creation
B. Processes
  3. Combination
    New parcels created by combination of simultaneous and sequential processes.
    New boundaries can have characteristics of either or both.
    Senior-junior standing may or may not exist
Description type
Quasi-metes and bounds;
“of”
Lot 1
Lot 2
Lot 3
Lot 6
Lot 5
Lot 4
Lot 1
Lot 2
Lot 3
Lot 6
Lot 5
Lot 4
New parcel is part of Lot 4
and part of Lot 5

## Slide 10: II. Rules of Construction (RoC)
Evaluation framework (aka Order of Importance of Conflicting Elements)
  Right of possession (unwritten rights)
  Senior right (in case of overlap)
  Written intentions of the parties (description)
  Call for survey
  Call for monuments; adjoiner
  Direction/distance
  Area/Coordinates
  If elements conflict, RoC indicates their relative weight
    Not strict; guidelines
    Description wording can change order
  If higher elements are lost, lesser elements carry greater weight.
Increasing weight
Particular
circumstances
Written
Record

## Slide 11: II. Rules of Construction (RoC)
A. Right of Possession: Unwritten Rights
  Based on adjacent owners actions/inactions
    Ownership departs from description
    Doctrines
      Adverse possession
      Prescription
      Oral agreement
      Equitable estoppel
      Recognition and acquiescence
    Ownership determined by courts
      Surveyor doesn’t have authority
      Map deed and use (encroachment) lines
Deed
Line
Ownership
Line
Unwritten
Right
Deed
Line
Fence

## Slide 12: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  Precedence establishment
    Once boundary is created, Sr-Jr relationship is established and doesn’t change unless boundary is legally removed.
      Is a boundary attribute, not an owner attribute
    Child inherits parent’s Sr-Jr standing along shared boundaries.
    Parent is junior to children – parent must provide.
    ≥2 adjoining children from common parent-
      overlap/gap potential
    Resolution depends on how parcels are created
Parent
Child
A
Child
B

## Slide 13: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  1. Simultaneous
    Parcel boundaries have equal standing: no sr-jr rights
    Excess or deficiency proportioned between found original corners
    Subdivision
    USPLS
      Single or Double Proportionate Measurement
125.0 ft
100.0 ft
150.0 ft
372.5 ft
Lot 1
Lot 2
Lot 3
Lot 1: W = (372.5/375.0) x 125.0 = 124.2 ft
Lot 2: W = (372.5/375.0) x 100.0 = 99.3 ft
Lot 3: W = (372.5/375.0) x 150.0 = 149.0 ft
 372.5 ft

## Slide 14: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  2. Sequential
    Earlier created boundaries have higher standing than later boundaries
Parent
Parcel
C: 2015
A: 2008
B: 2010
Jr
Sr
Jr Jr
Sr Sr
A:2008
Parent
Remainder
Jr
Sr
A: 2008
B: 2010
Jr
Sr
Jr Jr
Sr Sr
Parent
Remainder

## Slide 15: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  2. Sequential
    Child inherits parent’s sr-jr relationship along shared boundaries
C: 2015
A: 2008
B: 2010
Jr
Sr
Jr Jr
Sr Sr
C: 2015
B: 2010
Jr
Sr
Jr Jr
Sr Sr
A
Remainder
Jr
Sr
Sr
Jr
D: 2017
Inheritance
Parcel D description might call Parcel B as adjoiner but
Parcel D is senior by inheritance.

## Slide 16: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  2. Sequential
    Along sr-jr boundaries:
    • Sr parcel protected in case of an overlap - the junior parcel yields.
    • If excess, gap is parent remainder.
      Touchy situation: Give to one parcel or other or split between?
      Obviously original intent wasn’t for a gap to exist.
        “The question is not what reasonable men intended to convey but what they in fact described in the contract or memorandum.”
          Wiegand v. Gissal, 28 Wis. 2d 488, Wis. Supreme Court 1965
      The gap was not conveyed.
Parent
A: 2010
Sr
Jr
B: 2013
Parent
Remainder

## Slide 17: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  3. Combination
    Parcel boundaries may or may not have sr-jr relationships
    Example:
      Subdivision: simultaneous, no sr-jr relationships
200.00’
200.00’
200.00’
200.00’
200.00’
200.00’
Lot 11
Lot 13
Lot 12

## Slide 18: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  3. Combination
    Parcel boundaries may or may not have sr-jr relationships
    Example:
      Sequentially: “West 100.0 ft of Lot 12” later “East 100.0 ft of Lot 12”
200.00’
200.00’
200.00’
200.00’
200.00’
200.00’
Lot 11
Lot 13
Sr
Jr
W 100.0’
E 100.0’
No sr-jr relationships
along these lines.

## Slide 19: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  3. Combination
    Parcel boundaries may or may not have sr-jr relationships
    Example:
      Sequentially: “West 100.0 ft of Lot 12” later “East 100.0 ft of Lot 12”
      Resurvey: Deficiency on N, excess on S creates 2.0 ft remainder
200.00’
200.00’
200.00’
200.00’
200.00’
Lot 11
Lot 13
Sr
Jr
W 100.0’
E 100.0’
198.0’
202.0’
100.0’
98.0’
100.0’
100.0’
2.0’ Remainer
Sr
Jr
W 100.0’
E 100.0’

## Slide 20: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  3. Combination
    Parcel boundaries may or may not have sr-jr relationships
    Example:
      Instead: “West 100.0 ft of Lot 12” later “Lot 12 except West 100.0 ft”
200.00’
200.00’
200.00’
200.00’
200.00’
200.00’
Lot 11
Lot 13
Sr
Jr
W 100.0’
Lot 12
except
W 100.0’
No sr-jr relationships
along these lines.

## Slide 21: II. Rules of Construction (RoC)
B. Senior Right: Gap or Overlap
  3. Combination
    Parcel boundaries may or may not have sr-jr relationships
    Example:
      Instead: “West 100.0 ft of Lot 12” later “East 100.0 ft of Lot 12”
      Resurvey: Deficiency on N, excess on S to junior parcel
200.00’
200.00’
200.00’
200.00’
200.00’
Lot 11
Lot 13
Sr
Jr
W 100.0’
E 100.0’
198.0’
202.0’
100.0’
98.0’
100.0’
102.0’
Sr
Jr
W 100.0’
Lot 12
except
W 100.0’

## Slide 22: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    a. Statute of Frauds (SoF)
      Contract must be in writing to be valid.
      All terms included
      Prevents contradiction by action or word
      Interested third parties can interpret
      Deed is a contract for property conveyance
      Description defines physical extent and rights transferred
      Written intent
      What about unwritten rights?
        Courts do not view unwritten rights as title transfer but instead as title clarification.

## Slide 23: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    b. Description Interpretation
    Simultaneous: references to map or plat
      Unless errors on map, intent relatively clear
    Sequential or Combination: narrative descriptions
      Greater conflicts potential
      Archaic terms, “ancient” measurements
        “Commencing at a point 20 rods 19 links North of a point that is 26 links East of the East side of the steel tube at the Northeast corner of the wagon bridge...” (1992)
      Written by non-surveyors
        “Commencing at the West 1/4 corner of Section 9; thence N80° 29ft 17in. East, 2781.62 ft; thence S89° 11ft East, 177.84 ft;...” (1996)
    Surveyor must follow common law principles to interpret & apply description

## Slide 24: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    c. Controlling and Informative Terms
      Controlling: defines course termination and/or path
        Key words: to, along, parallel, perpendicular, with, continuing...
        Identify a condition
      Informative: all other terms, help identify controlling term(s)
      “..thence North 38 degrees West 139.6 feet to an iron stake...”
        Go to and end at the iron stake (to);
        Monument higher element, dist & dir yield if conflict.
      “...thence southwesterly along said high water mark to an iron stake...”
        Course follows topographic feature (along)
        and ends at an iron stake (to);

## Slide 25: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    d. Ambiguities
      (1) Extrinsic evidence
      Physical and parol evidence outside the description.
      Cannot be used to change description terms, only help explain.
      (2) Ambiguity Types
      Ambiguity: when something can be reasonably interpreted more than one way. Introduces confusion.
        Common in descriptions written by non-surveyors.

## Slide 26: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    d. Ambiguities
      (2) Ambiguity Types
      (a) Latent
        Hidden, not apparent until application.
        “Commencing at a point 84 1/4° East of the center of Section Seven (7); being station "A” having bearing tree viz; a black oak 14 inches in diameter, South 6° East 57 links distant, (said black oak being North 84 3/4° East, 24 7/25 rods of Stephen A. Thayer dwelling house),...” (1999)
        May need extrinsic evidence to reconstruct location

## Slide 27: II. Rules of Construction (RoC)
C. Written Intent
  1. Background
    d. Ambiguities
      (2) Ambiguity Types
      (a) Patent
        Obvious, immediately apparent
          “... thence S55° 55ft 20in West, 15.36 ft;"” (1999)
        Mistake in original contract.
        Mistake must be found and applied where it occurred.
        Correction instrument

## Slide 28: II. Rules of Construction (RoC)
C. Written Intent
  2. Call for survey
    Some boundary creations are based on survey and monumentation
      USPLS: survey before sale
      Subdivision plat: map and monument before sale
    Survey & map are primary evidence of intent.
      Typical for simultaneously created parcels.
  3. Monuments and Corners
    a. Monument v Corner
      Corner: legal location; dimensionless
      Monument: physical feature used to mark a corner
      Monument is corner surrogate, if it controls

## Slide 29: II. Rules of Construction (RoC)
C. Written Intent
  3. Monuments and Corners
    b. Monument
      (1) To control over lesser elements
        Must be
        Called in description
        Identifiable
        Undisturbed
        Can control
        Direction and termination
        Direction only; termination controlled by higher element
      (2) Accessories
        When established at original monument placement, are considered part of the monument.

## Slide 30: II. Rules of Construction (RoC)
C. Written Intent
  3. Monuments
    b. Monument
      (3) Disposition: Location certainty
      Existent (Found): position can be identified by original mon/acc or acceptable physical & parol evidence. Location is certain.
      Obliterated: no traces of original mon/acc, but position can be re-est beyond reasonable doubt using physical & parol evidence.
      Lost: Insufficient evidence to re-est beyond reasonable doubt. Must resort to measurements to surrounding corners.

## Slide 31: II. Rules of Construction (RoC)
C. Written Intent
  3. Monuments
    b. Monument
      (4) Corner by Common Report
      Location based on reputation
      Reasonable location
      Accepted by all affected parties
      Location can’t be disproved
        Avoid using this location justification. Based on unwritten rights.
        Evidence collection and evaluation.

## Slide 32: II. Rules of Construction (RoC)
C. Written Intent
  4. Measurements
    a. Distance and Direction
      Inferior to a controlling monument
      Control if:
      Monuments not called
      Called monuments are lost
      Direction basis? Can recreate in field?
      How numbers are written convey magnitude and implied accuracy.
        “North, 200 ft”
          How close to north? Distance to 100 ft, 10 ft, 1 ft?
        “...thence S88°16’52”W, 0.30 feet to the existing east line of Section 1, T5N, R9E; thence S00°18’01”W, 0.01 feet along said east line of Section 1;...” (2002)

## Slide 33: II. Rules of Construction (RoC)
C. Written Intent
  4. Measurements
    b. General directions
      Informative term
        A range of directions for each general one
W
E
S 22.5° E
N 22.5° E
N 67.5° E
S 67.5° E
N 22.5° W
N 67.5° W
S 67.5° W
S 22.5° W
Northerly
Easterly
Southerly
Westerly
Southwesterly
Southeasterly
Northeasterly
Northwesterly
S
N
“...to the northerly sideline of Maple Drive; thence easterly along said sideline...”

## Slide 34: II. Rules of Construction (RoC)
C. Written Intent
  4. Measurements
    c. What’s a conflict?
      Last two courses “... thence S18°20’W, 283.2 ft to a 1/2-inch iron pin; thence 220 ft back to the point of beginning.”
        All corners have been recovered until last one before POB.
        No mon evidence at S18°20’W, 283.2 ft, pt A.
        1/2-inch iron pin at S17°50’10”W, 285.72 ft, p B.
        A & B ~3 ft apart.
        POB to pt A is 220.5 ft, to pt B 224.52 ft.
      Are dist and dir to pt B “too far” from record dir and dist?
        Can lower elements control over higher elements?
      Does pt A fit closing line better than pt B?
        Is B-POB dist within the uncertainty of the 220 ft call?
        How much must elements differ to conflict with each other?
      Extrinsic evidence?
A
B

## Slide 35: II. Rules of Construction (RoC)
C. Written Intent
  5. Area/Coordinates
    a. Area
      USPLS: nominal or legal area. Actual area may be larger or smaller.
      Subdiv laws: areas included on plat
      Informative in both cases.
      M&B descriptions
      Area generally in summation
        “...said parcel containing 1.5 acres.”
        Informative
      Controls if intent was to convey specific amount.
        “...the Easterly 2 acres...”
        “...the southeasterly half...”

## Slide 36: II. Rules of Construction (RoC)
C. Written Intent
  5. Area/Coordinates
    b. Coordinates
      Coordinates, even with GPS, are derived quantities.
      Historically have either not been included or were informative.
      Times changing’:
        “...thence Northerly 487 feet, more or less, to GPS waypoint, Lat. 43.828655, Long. -90.661033; thence Northwesterly 296 feet, more or less, to GPS waypoint, Lat. 43.829424, Long. -90.661390; thence Westerly 298 feet more or less, to GPS waypoint, Lat. 43.829516, Long. -90.662515;...” (2005)
      No higher element calls.
      Controlling terms: to GPS waypoint
      Coordinate questions
        Units? Accuracy? Datum/adjustment?

## Slide 37: II. Rules of Construction (RoC)
C. Written Intent
  6. More or less
    Indicates an element has unknown certainty.
    The element is informative
    Similar terms: approximately, plus minus, ±, about
      “...thence running in an Easterly and Southeasterly direction along the South and Southwesterly line of private road that is used by the grantee herein a distance of about 28 rods; thence...” (2001)
    Need extrinsic evidence
Go to the last Stop sign and take a left.
How do I know
it’s the last one?

## Slide 38: II. Rules of Construction (RoC)
C. Written Intent
  7. Conflicting Title Elements
    “...Beginning at a 1-inch diameter iron bar in the north line of the Pohl property; thence N10°20’E 241 ft to a 1/2-inch iron pin; thence N85°35’E 267 ft to a 1/2-inch iron pin; thence S18°45’W 283 ft; thence back to the point of beginning”
  First two courses found with no issues. Diagram shows third course situation.
  How to run in last two courses?
  Assume no extrinsic evidence available.
Pohl
(senior property)
1/2-inch iron pin found at S17°50’36”W 282.91 ft. Pin is 2.0 ft south of Pohl’s line. Origin unknown.
No monument found at S18°45’W 283 ft. This location is 1.3 ft south of Pohl’s line.
Distance between the two positions is ~2.5 ft.
Pohl line

## Slide 39: II. Rules of Construction (RoC)
C. Written Intent
Short answer
Proceed at record S18°45’W, ~281.7 ft, to Pohl’s line and stop. Monument not called for, so it can’t control. Neither can the 283 ft distance since that would violate Pohl’s senior right.
Longer answer
Although we are looking for the termination of the third course, we can check the next course to see if it provides any additional informative terms, such as a distance back to the POB. In this case it doesn’t but if it did that might help.
Regardless, we know the third course must stop at Pohl’s senior line.
Does the monument have a controlling role? Why is it there? Accept because it’s like the others? Accept by Common Report?
Pohl
(senior property)
1/2-inch iron pin found at S17°50’36”W 282.91 ft. Pin is 2.0 ft south of Pohl’s line. Origin unknown.
No monument found at S18°45’W 283 ft. This location is 1.3 ft south of Pohl’s line.
Distance between the two positions is ~2.5 ft.
Pohl line

## Slide 40: II. Rules of Construction (RoC)
C. Written Intent
Longer answer continued
Are S17°50’36”W & 292.91 ft w/in uncertainty of record S18°45’W and 283 ft? Brng might not, but the dist is. Does that mean because distance fits that the bearing yields and the monument controls direction?
Without a monument call, that’s a tough sell.
Monument might be a potential unwritten rights ownership corner and line, but that’s not for the surveyor to decide.
May be a reason the monument exists, but nothing in the description gives it authority.
What sources of extrinsic evidence should be investigated?
Always identify plausible alternatives and explain why they aren’t acceptable.
Pohl
(senior property)
1/2-inch iron pin found at S17°50’36”W 282.91 ft. Pin is 2.0 ft south of Pohl’s line. Origin unknown.
No monument found at S18°45’W 283 ft. This location is 1.3 ft south of Pohl’s line.
Distance between the two positions is ~2.5 ft.
Pohl line

## Slide 41: Learning Objectives
How parcels and boundaries are created
Where the Rules of Construction come from
What are unwritten rights
How gaps and overlaps are handled
The Statute of Frauds and why it matters
Description interpretation issues: Ambiguities; Controlling/informative terms
Written intent conflicts

## Slide 42: Questions?

## Slide 43
That’s It!