## Slide 1: Session 27 GroundGrid - Simple, Right?
2025 WSLS Annual Institute
23 January 2005
Jerry Mahun, PLS
Thrice-retired
jerry.mahun@gmail.com
https://jerrymahun.com
SP
NP

## Slide 2: GridGround - Simple, Right?
I. Spatial Systems
II. Distortions
III. Earth Models
IV. Creating a Grid
V. Wisconsin Coordinate Systems
VI. Ground and Grid
VII. Grids and PLSS Lost Corners

## Slide 3: I. Spatial Systems

## Slide 4: I. Spatial Systems
A. Three-Dimensional
  1. Geodetic Coordinates
    Reference defined by ellipsoid and fit.
      NAD 83 - GRS 80 fit to Earth’s mass center.
      NAD 27 - Clarke 1866 fit to Meades Ranch, KS
P
Meridian
Normal
 | Normal | A line from the observer’s position, P, perpendicular to the ellipsoid
 | Meridian | An elliptical section containing the normal and semi-minor axes. Defines Geodetic N at a point.
 | Geodetic meridians converge. | 
Geo N
Geo S
Equator

## Slide 5: I. Spatial Systems
A. Three-Dimensional
  1. Geodetic Coordinates
    Longitude (λ) - Angle in Equatorial plane E or W from Greenwich Meridian
      0°-180°W; 0°-180°E
    Latitude (Φ) - Angle in meridian N or
      S of the Equator.
      0°-90°N; 0°-90°S
Geo N
Geo S
P
Normal
f
l

## Slide 6: I. Spatial Systems
A. Three-Dimensional
  1. Geodetic Coordinates
    Disadvantages:
      Positions are expressed in angular values
      Distances are in angular values
      Elliptical geometry
        Shortest distance between two points is a geodesic - shallow s-shape curve.
Geo N
Geo S
P
Q

## Slide 7: I. Spatial Systems
A. Three-Dimensional
  2. Terrestrial Coordinate System - TCS
    Three axis rectangular system
      Origin at Earth’s mass center
      Coordinates are linear values
X
Y
Z
Greenwich
Meridian
90° l

## Slide 8: I. Spatial Systems
A. Three-Dimensional
  2. Terrestrial Coordinate System - TCS
    Disadvantages:
      Huge coordinate values.
      Negative coordinates
      No “up” (vertical direction)
        Top and bottom of vertical structures have different 3D coordinates.
X
Y
Z

## Slide 9: I. Spatial Systems
B. Two Dimensional
  1. Planar
    Characteristics
      a. Orthogonal
      b. Parallel north lines
      c. Uniform scale in both directions
    Comps are simple.
    Disadvantage(s)?
North
East
1 unit
1 unit
90°
North
North
North

## Slide 10: I. Spatial Systems
North
East
B. Two Dimensional
  1. Planar
    Disadvantages
      We're on a 3D earth
      We want to put it in a 2D system

## Slide 11: I. Spatial Systems
North
East
B. Two Dimensional
  1. Planar
    Disadvantages
      We're on a 3D earth
      We want to put it in a 2D system

## Slide 12: I. Spatial Systems
North
East
B. Two Dimensional
  1. Planar
    Disadvantages
      We're on a 3D earth
      We want to put it in a 2D system
      With a direct projection we get a distorted representation

## Slide 13: I. Spatial Systems
B. Two Dimensional
  1. Planar
    Disadvantages
      We're on a 3D earth
      We want to put it in a 2D system
      With a direct projection we get a distorted representation
    Different mathematical projections distort different ways.

## Slide 14: II. Distortions

## Slide 15: II. Distortions
A. Projection Area
  The smaller the area projected, the smaller the distortions.
E
N
Grid (2D) - Solid red
Geodetic (3D) - Dashed blue

## Slide 16: II. Distortions
B. Types
  The two primary distortions are
    1. Direction
      3D meridians converge, 2D do not.
      3D E/W lines are curved, 2D are straight.
      No distortion at center of projection
      Increases moving E & W of center
      g: convergence; angle between grid and geodetic north
E
N
Grid (2D) - Solid red
Geodetic (3D) - Dashed blue
g
g
g
g
Direction distortion

## Slide 17: II. Distortions
B. Types
  The two primary distortions are
    2. Distance
      Ground points must be projected vertically to the 2D grid plane.
      This moves them closer together or further apart, altering distance.

## Slide 18: II. Distortions
C. Compensation
  Except for extremely small areas, projecting 3D to 2D will always create direction and distance distortions.
  They are systematic errors - can be compensated mathematically as long as we know how the surfaces are mathematically connected.
  For that, we need some earth models.
g
g
g
g

## Slide 19: III. Earth Models
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 20: III. Earth Models
A. Physical Earth - Ground
    The surface on which we measure.
      Not mathematical.
      Over small areas, we can assume a flat reference system - plane; simple grid
      Over larger areas, must account for earth's shape and dynamics - curved reference
        Must then project from curved surface to a flat grid.
        Need some to connect mathematically

## Slide 21: III. Earth Models
B. Geoid
    An equipotential surface defined by gravity (in) and centrifugal force (out).
    Gravity = f(mass)
      Earth: non-homogeneous; mass anomalies
       Lines of gravity are neither parallel nor straight.
    Geoid is a lumpy and changing nonmathematical surface.
SP
NP

## Slide 22: III. Earth Models
B. Geoid
    Gravity is perpendicular to the geoid
      Centering a bubble or using a plumb bob orients equipment to the geoid.
    Geoid approximates sea level datum
      Connected to physical Earth by elevations - orthometric heights
Physical
Geoid
Where we are
What we
reference to.

## Slide 23: III. Earth Models
C. Ellipsoid
    Mathematical 3D surface
    Fit to geoid
      Doesn’t fit exactly; compromises
Physical
Geoid
Ellipsoid

## Slide 24: III. Earth Models
    Skewness - Deflection of the vertical, d
      Angle between directions of gravity and ellipsoid normal.
C. Ellipsoid
    Geoid - Ellipsoid fit at a point is a function of Skewness and Vertical separation.
Physical
Geoid
Ellipsoid

Normal

## Slide 25: III. Earth Models
  Vertical separation
    Heights between the surfaces
      H - Orthometric: geoid to ground
      N - Geoid: ellipsoid to geoid
      h - Ellipsoidal: ellipsoid to ground
    h = H+N
C. Ellipsoid
    Geoid - Ellipsoid fit at a point is a function of Skewness and Vertical separation.
Physical
Geoid
Ellipsoid
g
h
N
H

## Slide 26: III. Earth Models
D. Grid
  The final surface is a grid
    Can be more than one depending on coordinate systems needed.
    Move points from ground, through geoid and ellipsoid, to the grid
Physical
Geoid
Ellipsoid
Grid

## Slide 27: IV. Creating a Grid

## Slide 28: IV. Creating a Grid
A. Projection Surfaces
  Grid is based on a Projection Surface which is fit to Ellipsoid
Cone
Cylinder

## Slide 29: IV. Creating a Grid
B. Lambert Conic Conformal
    Cone placed over (and through) ellipsoid.
    Points projected.
    Projection is laid out flat and a coordinate system overlaid.
N
E
Central
Meridian
Geodetic
N

## Slide 30: IV. Creating a Grid
B. Lambert Conic Conformal
    Distance distortion
    Scale, k, is constant E/W; varies N/S
N
E
k>1
k>1
k<1
k=1
k=1
G
H
G'
H'
k<1
Grid
Ellipsoid
L
M
L'
M'
k>1
Grid
Ellipsoid

## Slide 31: IV. Creating a Grid
B. Lambert Conic Conformal
    Direction distortion
      Convergence, g, is angle between Grid and Geodetic North.
        0° at CM, increases to E and to W
N
E
Geodetic
N
Grid
g
Grid
g
Grid
g

## Slide 32: IV. Creating a Grid
C. Mercator Transverse Cylindric
    The projection surface is “rolled” out.
        Central Meridian defines Grid North
    Distance distortion
    Scale, k, is constant N/S; varies E/W
(0, 0)
North
East
Grid N
True N
k < 1
k > 1
k > 1
k = 1
k = 1
Central
Meridian

## Slide 33: IV. Creating a Grid
C. Mercator Transverse Cylindric
    Direction distortion
      Convergence, g, is angle between Grid and Geodetic North.
        0° at CM, increases to E and to W
Geodetic N
Grid
Grid
N
E
Central
Meridian
g
g

## Slide 34: V. Wisconsin Coordinate Systems

## Slide 35: V. Wisconsin Coordinate Systems
1. State Plane Coordinate (SPC) system
2. Universal Transverse Mercator (UTM)
A. Nationally Defined & Supported
Projection | Conic
Zones | 3
Max Distortion (ellipsoid to grid) | 1/10,000
Projection | Cylindric
Zones | 2
Max Distortion (ellipsoid to grid) | 1/2500

## Slide 36: V. Wisconsin Coordinate Systems
1. Wisconsin Transverse Mercator (WTM) System
Developed by WisDNR to facilitate statewide coverage on a single coord grid.
Modified UTM
  Cylindric projection rotated 3° placing it halfway between UTM Zones 15 & 16.
WisDNR data is generally provided in WTM system.
B. Locally Defined and Supported
Projection | Cylindric
Zones | 1
Max Distortion (ellipsoid to grid) | 1/2500

## Slide 37: V. Wisconsin Coordinate Systems
2. Low Distortion Projections
a. WCCS - Wis County Coord Systems
  Original design.
  All projections used raised ellipsoids
    GRS80 + Ave Geoid ht + Median elev
  `
    Results in non-standard ellipsoid
      Different datum
      Caused problems with some software.
B. Locally Defined and Supported
Projection | Cylindric & Conic
Zones | 58
Max Distortion (ground to grid) | urban: 1/50,000 rural: 1/30,000
Grid
Ground
Raised Ellipsoid
GRS80 Ellipsoid

## Slide 38: V. Wisconsin Coordinate Systems
2. Low Distortion Projections
b. WisCRS - Wis Coord Reference Systems
  WCCS redefinition
  Same zones but each used GRS 80 ellipsoid directly.
    Maintains accuracy with respect to WCCS.
      Allowable design difference: ± 5 mm
B. Locally Defined and Supported
Projection | Cylindric & Conic
Zones | 58
Max Distortion (ground to grid) | urban: 1/50,000 rural: 1/30,000
Ground
Grid
GRS80 Ellipsoid

## Slide 39: VI. Ground and Grid
What's the beef?

## Slide 40: VI. Ground and Grid
1. Distance
  Two steps
  a. Ground to ellipsoid
A. Distortion Compensation
dH | Horizontal ground distance
dE | Ellipsoidal (geodetic) distance
EF | Elevation Factor
R | Mean earth radius
H | Orthometric ht (elev)
N | Geoid height
k | Scale factor
R = 20,902,000 ft = 6,371,000 m (approx.)
R
N
H
Ellipsoid
Geoid
Ground
dH
dE

## Slide 41: VI. Ground and Grid
1. Distance
  Two steps
  b. Ellipsoidal to grid
  c. Combined factor
A. Distortion Compensation
dG | Grid distance
dE | Ellipsoidal (geodetic) distance
k | Grid scale factor
R
N
H
Ellipsoid
Geoid
Ground
dH
dE
dG
Grid
`
`

## Slide 42: VI. Ground and Grid
1. Distance
  c. LDP
    Because a LDP grid is near-ground level, there may be no discernible difference between ground and grid distances.
    Most of the time, this reduction can be ignored for both WCCS and WisCRS grids.
A. Distortion Compensation
R
N
H
Ellipsoid
Geoid
Ground
dH
dE
dG
LDP
`
`

## Slide 43: VI. Ground and Grid
2. Direction
  The convergence angle, g, is from Geodetic N to Grid N
  It is positive (cw) East of the CM, negative (ccw) West of the CM
  To convert Geodetic (Ground) direction to Grid:
  Might be significant for an LDP
A. Distortion Compensation
t | Grid azimuth
a | Geodetic azimuth
g | Convergence
Grid N
Geod N
Geod N
Grid N
Central
Meridian
Geod N
Grid N
A
B
gA
gB

## Slide 44: VI. Ground and Grid
  Where do we get the ortho and geoid heights, scale, and convergence angles?
  NGS software (Geodetic Tool Kit):
    NCAT1
    GEOIDXX
  Ortho heights from USGS topoquads
  1NCAT does not currently support local LDPs. When NATRF2022 is adopted, NCAT will include NGS-accepted LDPs.
B. Reduction Elements

## Slide 45: VI. Ground and Grid
B. Reduction Elements
  NSRS
  Datasheet
DESIGNATION - JERRY
PID - NH0936
______________________________________________________________________
* NAD 83(2011) POSITION- 42 54 24.02215(N) 089 43 53.76413(W) ADJUSTED
* NAD 83(2011) ELLIP HT- 324.836 (meters) (06/27/12) ADJUSTED
* NAD 83(2011) EPOCH - 2010.00
* NAVD 88 ORTHO HEIGHT - 358.6 (meters) 1177. (feet) VERTCON
______________________________________________________________________
GEOID HEIGHT - -33.902 (meters) GEOID18
NAD 83(2011) X - 21,919.631 (meters) COMP
NAD 83(2011) Y - -4,679,204.603 (meters) COMP
NAD 83(2011) Z - 4,320,134.562 (meters) COMP
LAPLACE CORR - -0.36 (seconds) DEFLEC18
North East Units Scale Factor Converg.
SPC WI S - 100,758.292 621,917.891 MT 0.99996957 +0 11 03.9
SPC WI S - 330,571.16 2,040,408.95 sFT 0.99996957 +0 11 03.9
UTM 16 - 4,754,071.382 277,008.712 MT 1.00021177 -1 51 37.6
- Elev Factor x Scale Factor = Combined Factor
SPC WI S - 0.99994906 x 0.99996957 = 0.99991863
UTM 16 - 0.99994906 x 1.00021177 = 1.00016082
At Jerry's elevation

## Slide 46: VI. Ground and Grid
1. Elevation factor, EF
    N doesn't change much so can generally use a single value over the project area.
    Depending on terrain, H can be:
      project area average – use for all lines
      computed average for each line
  2. Grid scale, k
    For relatively small projects, a single value at project center could be used.
    Larger/longer projects would require applying different k in different areas.
    SPC/UTM - use approx. lat & long with NCAT to determine k.
C. Variations

## Slide 47: VI. Ground and Grid
  Quarter line NW-N1/4 of Sec 34 T5N R7E
    Distance: 2638.25 ft
    Bearing: S88°11’34”E
  Determine WI SPC South zone grid distance and bearing from NW to N1/4
  From topoquad
    NW elev: 960 ft
    N1/4 elev: 1050 ft
    Approx position of NW corner is:
      42°57.5' Lat
      89°39.75' Long
D. SPC Example
N1/4
NW

## Slide 48: VI. Ground and Grid
  Quarter line NW-N1/4 of Sec 34 T5N R7E
    Distance: 2638.25 ft
    Bearing: S88°11’34”E
  Determine WI SPC South zone grid distance and bearing from NW to N1/4
  From topoquad
    NW elev: 960 ft
    N1/4 elev: 1050 ft
    Approx position of NW corner is:
      42°57.5' Lat
      89°39.75' Long
D. SPC Example
From NCAT
  k = 0.99996 224
  g = +0°13'53.46"
From GEOID18
  N = -34.046 m
N1/4
NW

## Slide 49: VI. Ground and Grid
  1. Distance
    a. Ground to ellipsoid
D. SPC Example
R = 20,902,000 ft
From NCAT
  k = 0.99996 224
  g = +0°13'53.46"
From GEOID18
  N = -34.046 m = -111.7 ft
N1/4
1050 ft
NW
960 ft
2638.25 ft

## Slide 50: VI. Ground and Grid
  1. Distance
    a. Ground to ellipsoid
    b. Ellipsoid to grid
D. SPC Example
R = 20,902,000 ft
From NCAT
  k = 0.99996 224
  g = +0°13'53.46"
From GEOID18
  N = -34.046 m = -111.7 ft
N1/4
1050 ft
NW
960 ft
2638.25 ft

## Slide 51: VI. Ground and Grid
  2. Direction
    Convert bearing to azimuth
    Convert to Grid Az
    Convert to bearing
D. SPC Example
R = 20,902,000 ft
From NCAT
  k = 0.99996 224
  g = +0°13'53.46"
From GEOID18
  N = -34.046 m = -111.7 ft
N1/4
1050 ft
NW
960 ft
S88°11’34”E

## Slide 52: VI. Ground and Grid
1. Reduction Elements
  LDPs are not supported by NCAT, how to get N, convergence, and scale?
  N: Use GEOIDXX, but need geodetic coordinates.
  g and k: ?
    Need LDP-specific software.
    Some surveying and mapping software have support for LDPs, including Wisconsin's.
E. WCCS/WisCRS

## Slide 53: VI. Ground and Grid
2. ConCoord v0.95
At https://jerrymahun.com
E. WCCS/WisCRS

## Slide 54: VI. Ground and Grid
3. Wis83CoordConv1-5.xlsm
At https://jerrymahun.com
E. WCCS/WisCRS

## Slide 55: VI. Ground and Grid
  NSRS point Jerry to W1/4 cor Sec 13 T5N R6E
    Distance: 2313.88 ft
    Azimuth: 283°39'44"
    Elev: 1050 ft (topoquad)
  What are the distance and direction in the WisCRS Dane County Coord System?
  Jerry's data sheet has H and N, but not Dane Co coords data.
    Must compute needed elements.
    Use Jerry's Lat and Long in ConCoord.
Pt Jerry
  42°54'24.02215" Lat
  89°43'53.76413" Long
  H = 1177 ft
  N = -33.902 m = 111.2 ft
F. WisCRS Example
Jerry
1177 ft
W1/4
1050 ft

## Slide 56: VI. Ground and Grid
F. WisCRS Example

## Slide 57: VI. Ground and Grid
  1. Distance
  2. Direction
F. WisCRS Example
Jerry
1177 ft
W1/4
1050 ft
k: 1.00004 24995
g: -0°12'40.6"
2313.88 ft
283°39'44" Az

## Slide 58: VI. Ground and Grid
  1. Distance
  2. Direction
    Distance distortion?
        Can ignore reduction
F. WisCRS Example
Jerry
W1/4
2313.88 ft
283°52'25" Az

## Slide 59: VII. Grids and PLSS Lost Corners

## Slide 60: VII. Grids and PLSS Lost Corners
Proportionate Measurement
  Recreating original locations based on record and contemporary measurements.
    Proportioning.
  PLSS Manual states that proportioning must be done in cardinal directions
      True N/S & True E/W
      (2009 Manual treats Geodetic and True the same, which isn’t technically correct, but close enough.)
A. Cardinal Equivalents
B
D
C
A

## Slide 61: VII. Grids and PLSS Lost Corners
Proportionate Measurement
  If working in a grid system must compensate for convergence.
    Before or after proportioning?
    How?
      g = f(Longitude) - it's not constant along E/W lines
    Is its effect significant?
A. Cardinal Equivalents
C
D
A
B
Grid
True

## Slide 62: VII. Grids and PLSS Lost Corners
1. Compensate Before Proportioning
  Compute grid bearings from coordinates
  Determine convergence at each point
  Convert grid to true directions
    True directions are not exactly 180° apart
B. Double Proportionate Procedure
C
D
A
B
TN
TN
TN
TN
Grid
True
Grid
True
g1
g2
=

## Slide 63: VII. Grids and PLSS Lost Corners
1. Compensate Before Proportioning
  PLSS Manual: use mean bearing of a line for its cardinal computations.
  Compute the true bearings at line midpoints.
  Then compute cardinal equivalents.
  Continue regular DPM process.
B. Double Proportionate Procedure
C
D
A
B
TN
TN
TN
TN

## Slide 64: VII. Grids and PLSS Lost Corners
2. Compensate After Proportioning
  Set temporary points using grid equivalents
B. Double Proportionate Procedure
N-S | Grid BrngAB | Grid DistAB
 | Grid LatAB | Grid DepAB
Set TN by SPM |  | 
E-W | Grid BrngCD | Grid DistCD
 | Grid LatAB | Grid DepAB
Set TE by SPM |  | 
Compute gN and gE at the temp points. |  | 
TN
TE
C
D
B
A
Grid Lat
Grid Dep

## Slide 65: VII. Grids and PLSS Lost Corners
2. Compensate After Proportioning
  At the two temporary points project lines rotated gN and gE from Grid N and Grid E.
  Set lost corner at intersection of the lines.
B. Double Proportionate Procedure
TN
TE
C
D
B
A
P
TN
TE
P
gN
gE
Grid N
Grid E

## Slide 66: VII. Grids and PLSS Lost Corners
ID | Corner | North (ft) | East (ft) | g
A | SW S9 | 352,289.81 | 711,348.81 | -0°24'32"
B | W1/4 S4 | 360,188.90 | 711,493.25 | -0°24'33"
C | SW S5 | 357,550.43 | 706,134.07 | -0°25'25"
D | SE S4 | 357,607.73 | 716,672.60 | -0°23'46"
g computed using ConCoord, |  |  |  | 
Does ignoring convergence affect corner position?
Example: Shawano County
  SW cor S4 T29N R11E is lost.
  Existing corners and their Shawano Co WisCRS coordinates are:
C. Significant Effect?
B
D
C
A

## Slide 67: VII. Grids and PLSS Lost Corners
Does convergence have a significant effect?
Computed values
Coordinates are close, but the two positions are 0.39 ft apart.
  Enough for a pin cushion.
Pt | North (ft) | East (ft) | g
TN | 357,556.08 | 711,348.74 | -0°24'33"
TE | 357,550.43 | 711,403.34 | -0°24'33"
C. Significant Effect?
B
D
C
A
Pt | North (ft) | East (ft) | Convergence
SW4 | 357,556.08 | 711,403.34 | Not applied
SW4 | 357,555.69 | 711,403.37 | Applied

## Slide 68: GridGround - Simple, Right?
I. Spatial Systems
II. Distortions
III. Earth Models
IV. Creating a Grid
V. Wisconsin Coordinate Systems
VI. Ground and Grid
VII. Grids and PLSS Lost Corners